## Slide 1: Converting Sugarcane Bagasse into Paper
A Step-by-Step Guide to Sustainable Production

## Slide 2: Step 1: Collection & Depithing
• Collection: Gathering waste from sugar mills.
• Depithing: Mechanical removal of the soft 'pith' core.
• Result: High-quality cellulose fibers ready for processing.

## Slide 3: Step 2: Digestion (Pulping)
• Process: Cooking fibers in a pressurized 'Digester'.
• Chemical Action: Using caustic soda to dissolve Lignin.
• Outcome: Separation of cellulose into a raw brown pulp.

## Slide 4: Step 3: Washing & Screening
• Washing: Removing 'black liquor' (spent chemicals).
• Screening: Filtering out knots, dirt, and uncooked particles.
• Quality Control: Ensures a smooth and uniform pulp texture.

## Slide 5: Step 4: Bleaching (Optional)
• Objective: Achieving high brightness for printing paper.
• Eco-Friendly Methods: Using ECF or TCF (Chlorine-free) techniques.
• Raw Finish: Often skipped for brown packaging materials.

## Slide 6: Step 5: Refining & Stock Prep
• Beating: Mechanically fraying fibers to improve bonding.
• Additives: Mixing in sizing agents, fillers, or dyes.
• Ready for Machine: The pulp is now 'Stock' ready for the wire.

## Slide 7: Step 6: Sheet Forming & Pressing
• Forming: Spraying diluted pulp onto a moving wire mesh.
• Drainage: Gravity and vacuums remove water to felt the fibers.
• Pressing: Heavy rollers squeeze out moisture and densify the sheet.

## Slide 8: Step 7: Drying & Finishing
• Drying: Passing over steam cylinders to evaporate water.
• Calendering: Polished rollers create a smooth surface.
• Winding: Final paper is rolled and cut for distribution.